## Slide 1: W3C Web of Things Security Testing Plan
Michael McCool and Elena Reshetova
January 30, 2019

## Slide 2: Draft W3C Note
See
  https://github.com/w3c/wot-security-testing-plan
Rendered version:
  https://cdn.staticaly.com/gh/w3c/wot-security-testing-plan/master/index.html
To be submitted for publication at the same time as the CR transition
The WoT charter only requires a security testing plan
  Not actual test results
Some "demonstration" security testing might be useful, however
  There is not really a single test suite that will work for all implementations

## Slide 3: WG Charter: Security Deliverables
In order to enhance the security of WoT systems, we will also generate and implement a security testing plan which will include both functional and adversarial testing of the proposed standards and their implementations.
We will only recommend an implementation of the proposed standards for use in production once it has passed such testing.

## Slide 4: Document Outline
Introduction
Best Practices
Functional Security Testing
Adversarial Security Testing
  Static Vulnerability Discovery
    Static Code Analysis
    Known vulnerability checking
  Runtime (Dynamic) Vulnerability Discovery
    Fuzz Testing
    Protocol Analysis
    Vulnerability Scanners
  Exploitation
Security Testing Plan Framework
Suggested Testing Frequency
Terminology
Summary
References
  Normative references

## Slide 5: Functional Security Testing
Related to "Behavioral" assertions for security in spec:
  Security mechanisms supported by a Thing should be consistent with its description in its Thing Description
  Generally, we cannot constrain a server, which may be pre-existing device…
    TD cannot "correct" insecure behavior by a described Thing
    A TD should describe exactly what the Thing does and needs, no more or less
    If the TD does not correctly describe a Thing, then the TD is incorrect, not the Thing
"Functional Testing" just checks for correct implementation of described security mechanisms:
  Accesses with proper authentication should be allowed
  Accessed without proper authentication should be denied
  Correct encryption and authentication mechanisms should be used

## Slide 6: Adversarial Security Testing
Mimics what an attacker would try to do
  We can re-use tools intended for attacking web services, although we should extend these with tools for IoT protocols (CoAP, MQTT, etc).
Three stages:
  Information gathering
  Vulnerability discovery
  Exploitation
Adversarial testing focuses on Vulnerability Discovery
  We assume the attacker has FULL knowledge of the target, potentially including source code, and of course the information in the TD
  Knowing how or whether a vulnerability is exploitable is important to testing only to prioritize which vulnerabilities should be fixed first (since we are not actually trying to break into the system)

## Slide 7: Discovering Vulnerabilities (1)
Static Code Analysis
  Tools with access to source code can find coding practices likely to lead to vulnerabilities, such as missing boundary checks on arrays accesses, lack of input validation, etc.
    Example tools: Klocwork, Coverity, Checkmarx.
  With access to the binary or library/package list, known vulnerabilities in any libraries used can be checked.
    Example tools: Protecode, OWASP's Dependency-Check, Snyk, npm audit.

## Slide 8: Discovering Vulnerabilities (2)
Runtime/Dynamic Code Analysis
  Does not require access to source, just external (network) interfaces
Fuzz Testing: Send randomly-generated inputs to interfaces, designed to bypass early checks (eg for protocol, JSON syntax checks, etc.) but trigger errors (eg buffer overruns, unexpected parameters, etc) in backend code.
  Example HTTP tools: Burp Suite, Wfuzz, Wapiti.
  Example CoAP tools: FuzzCoAP, CoAP Peach Pit.
  Example MQTT tools: ?
Protocol Analysis: Look at data on wire, look for misconfigured headers, etc. Often manual, but some scripted tools available.
  Example tools: Wireshark, tcpdump.

## Slide 9: Discovering Vulnerabilities (3)
Runtime/Dynamic Code Analysis
  Does not require access to source, just external (network) interfaces
Protocol Analysis: Look at data on wire, looking for misconfigured headers, insecure encryption options or combination of options, etc. Often manual, but some scripted tools available.
  Example tools: Wireshark, tcpdump.

## Slide 10: Discovering Vulnerabilities (4)
Runtime/Dynamic Code Analysis
  Does not require access to source, just external (network) interfaces
Vulnerability Scanner: Attempt to run a known set of exploits or vulnerability trigger inputs against the target and report the outcomes.
  Example tools: w3af, Burp vulnerability scanner, Nikto, WATOBO.

## Slide 11: Security Testing Plan Framework
Static Vulnerability Discovery:
  Static Code Analysis: If source code is available, a static code checker should be used to check for vulnerabilities in new purpose-written code.
  Known Vulnerability Checking: If binaries and/or a list of package dependencies are available, a vulnerability checker should be used to check for known vulnerabilities in libraries used.
Runtime Vulnerability Discovery: Appropriate tools such as Fuzz Testing, Protocol Analysis, and Vulnerability Scanners can be discover problems even when only the network interface is available, and are complementary to other kinds of checks.
Exploitation Analysis: This can be used to prioritize which vulnerabilities should be addressed first or whether a given vulnerable system can even be used in a given environment.

## Slide 12: Suggested Testing Frequency
Static Vulnerability Discovery: Should be done regularly, ideally integrated into the development work flow for a WoT component. This is important, since any even small code changes can introduce development mistakes, or alternatively new vulnerabilities can be discovered in the libraries that a program depends on. New vulnerabilities are discovered in existing libraries almost daily.
Runtime Vulnerability Discovery: Should be also done on a regular basis, for example for each major release or development milestone.
Exploitation Analysis: Should be done occasionally, whenever possible. It is the most time and resource consuming activity, often requires external resources with specialized knowledge, and cannot in general be automated.

## Slide 13: Summary
Have created a first draft of a testing plan; please review
Provides a framework and a set of tool categories
Lists example tools in each category
Does not provide a "universal testing plan" for all possible WoT systems; this is not feasible
We should, however, do some "demonstration" adversarial testing against WoT systems
  We did not do this at this TestFest, unfortunately, but should do at least some basic testing against specific systems as soon as possible.
Limitations:
  Few tools for CoAP, MQTT; plan does not consider physical attacks.